## Slide 1
SSCS Chipathon 2026 · Track A · Schematic Review
SFE Audio Frontend Spiking Frequency Encoder Bank
32-Channel Neuromorphic Encoder · GF180MCU · LibreLane 3.0
TeamVKU · Hoang Vu · github.com/hoangvu10105/chipathon-2026-teamvku

## Slide 2
Agenda
1
Project Overview & Motivation
2
Top-Level Architecture
3
SFE Channel: Integrate-and-Fire Neuron
4
AER Event Packetizer & FIFO
5
Fanout Buffer Tree
6
Padring Interface & Pin Assignment
7
Build Results & Metrics
8
Open Issues & Mitigations

## Slide 3
1. Project Overview
What is the Spiking Frequency Encoder?
The SFE converts parallel input data into sparse spike-event streams using 32 adaptive integrate-and-fire neurons. Each channel implements bio-inspired neural dynamics: membrane accumulation, leakage, adaptive threshold, and refractory period. Output uses standard AER protocol for direct integration with neuromorphic processors.
32
Frequency Channels
16-bit
Data Width per Channel
Adaptive
Threshold (16–1024)
AER
Address Event Representation
GF180MCU
180nm Open-Source PDK
0.018W
Total Power (TT corner)

## Slide 4
2. Top-Level Architecture
chip_top.sv — GF180MCU Padring (2935×2935 µm)
chip_core.sv — Pad Adapter + Reset Sync + Stimulus Generator
sfe_audio_frontend_top.sv — Top-Level SFE Wrapper
sfe_encoder_bank.sv — 32× SFE Channels + Fanout Buffers
sfe_event_packetizer.sv — AER Encoder + FIFO(16)
sfe_channel.sv ×32
sfe_fanout_ buffer.sv
60×Analog Pads | 20×Bidir Pads | 4×DVDD + 4×DVSS | clk + rst_n | 4×Corner

## Slide 5
3. SFE Channel: Integrate-and-Fire Neuron
The core computational unit — repeated 32×
x[n] 16-bit Input
Σ Membrane Accumulator
θ Compare: membrane ≥ theta?
↑↓ Spike Up/Down
↻ Refractory Counter
DATA_WIDTH
16
Input sample width
THETA_WIDTH
16
Adaptive threshold width
LEAK_SHIFT
4
Leakage: membrane >> 4 per tick
THETA_DEC_SHIFT
6
Threshold adaptation rate
REFRACTORY_LEN
4
Refractory period (cycles)
THETA_MIN / MAX
16 / 1024
Threshold bounds
THETA_INIT
32
Initial threshold

## Slide 6
4. AER Event Packetizer & FIFO
Address Event Representation — industry standard
AER encodes spike events as {channel_address, direction, timestamp} tuples. Priority encoder resolves simultaneous spikes; FIFO(16) buffers output events.
32× Spike In
Priority Encoder
Event Pack
FIFO (Depth 16)
AER Output
Output Interface
event_valid
1
Event data valid strobe
event_channel
5
Source channel [0–31]
event_direction
1
0=spike_down, 1=spike_up
event_timestamp
32
Monotonic event counter
fifo_full
1
FIFO at capacity
fifo_overflow
1
Event dropped
fifo_level
5
Current FIFO fill level

## Slide 7
5. Fanout Buffer Tree
Solving max_fanout violations on high-fanout control signals
Problem: Control signals (rst_n, en, cfg_*) drive all 32 channels simultaneously → 891 loads on single net → 182ns slew @ SS corner → 2470 violations. Solution: sfe_fanout_buffer limits fanout to MAX_FANOUT=10 per stage. Each bit of multi-bit signals gets its own buffer tree.
in
buf_0 → out[0:9]
buf_1 → out[10:19]
buf_2 → out[20:29]
Signals buffered by sfe_fanout_buffer:
en, rst_n, cfg_enable_adaptive, cfg_enable_leakage, cfg_enable_refractory, decay_tick, cfg_load (1-bit) cfg_theta_min[15:0], cfg_theta_max[15:0], cfg_theta_init[15:0], cfg_refractory_len (multi-bit, per-bit trees)
Buffer Tree Resource Cost:
7 × 1-bit buffer trees (fanout 32 each) + 16×THETA_WIDTH + 16×THETA_WIDTH + 16×THETA_WIDTH + REFRACTORY_WIDTH multi-bit trees = ~100 buffer instances total. Negligible area impact (<0.1%).

## Slide 8
6. Padring Interface & Pin Assignment
Workshop Slot — 2935×2935 µm die
analog (asig_5p0)
60
Reserved for future AFE
bidir (bi_24t)
20
4× config IN + 16× status OUT
DVDD / DVSS
4+4
Core and I/O power
clk_pad (in_s)
1
25 MHz system clock
rst_n_pad (in_c)
1
Active-low async reset
corner
4
Auto-inserted by LibreLane
Bidir Pad Assignment
bidir[3:0]
IN
run_en, fixed_threshold, decay_tick_2, disable_refractory
bidir[4]
OUT
event_valid
bidir[5]
OUT
event_direction
bidir[10:6]
OUT
event_channel[4:0]
bidir[17:11]
OUT
event_timestamp[6:0]
bidir[18]
OUT
overflow_flag (fifo_full | overflow)
bidir[19]
OUT
heartbeat (1 Hz toggle)

## Slide 9
7. Build Results
LibreLane 3.0 + GF180MCU PDK 1.8.0 · 2026-06-23
✅ 0
Lint Errors
✅ 0
Timing Violations (setup/hold)
129,874
Instances
7.81M µm²
Design Area
0.018 W
Total Power (TT 25°C 5.0V)
85 MB
Final GDS Size
~2h 15m
Full Signoff Build Time
⚠ 2470
Max Slew @ SS (Fix Applied)
⚠ 65/22
Fanout/Cap Violations

## Slide 10
8. Open Issues & Mitigations
⚠
Max Slew Violations (SS corner)
2470 violations, 182ns on rst_core_n
✅ Reset buffer tree added to chip_core.sv; SYNTH_MAX_FANOUT=10; MAX_TRANSITION_CONSTRAINT=3.0; rebuild pending
⚠
Max Fanout / Max Cap Violations
65 fanout + 22 cap violations across all corners
✅ SYNTH_MAX_FANOUT=10 in config.yaml; post-PNR repair_design pass enabled
ℹ
Cocotb Simulation
PDK path resolution issue in testbench
Fix PDK_ROOT path mapping; run make sim inside Docker container
📋
Analog Frontend
60 analog pads currently unused
Future phase: integrate analog filterbank frontend
📋
Chip ID / Logo Macros
Not included in current build
Enable MACROS section in config.yaml for tapeout submission
Next: Rebuild with slew fix → Run cocotb sim → Week 28 Simulation Review (blocks) → Week 29 Go/No-Go

## Slide 11
Thank You
SFE Audio Frontend — 32-Channel Spiking Frequency Encoder TeamVKU · Track A · SSCS Chipathon 2026
github.com/hoangvu10105/chipathon-2026-teamvku
Issue #167 · Discord: #2026-track-a-foundational-building