## Slide 1
SSCS Chipathon 2026 — Track A
SFE Audio Frontend Spiking Frequency Encoder Bank
32-Channel Neuromorphic Frequency Encoder on GF180MCU
TeamVKU · Hoang Vu · June 2026

## Slide 2
Project Overview
The SFE (Spiking Frequency Encoder) is a bio-inspired neural encoding block that converts parallel input data into sparse spike-event streams. Each of the 32 channels acts as an adaptive integrate-and-fire neuron with configurable threshold, leakage, and refractory period. Events are encoded in the industry-standard AER (Address Event Representation) protocol, enabling direct integration with neuromorphic processors.
32 Channels
16-bit frequency-encoded filterbank
Adaptive Threshold
Self-tuning theta (16–1024)
AER Output
Address Event Representation industry standard
GF180MCU
180nm open-source GlobalFoundries PDK
Audio In → Filterbank → SFE Core → AER Packetizer → Bidir Pads (32-ch, 16b) (Adaptive) (FIFO 16) (20 pads)

## Slide 3
Block Diagram
sfe_audio_frontend_top
sfe_encoder_bank (×32 channels)
sfe_event_packetizer
AER · FIFO · Priority
sfe_fanout_buffer
(max fanout ≤ 10)
sfe_channel (×32)
Integrate-Fire Neuron
chip_core
Pad Adapter
Workshop Padring
60×Analog · 20×Bidir · PWR

## Slide 4
Technical Specifications
Process
GF180MCU (180nm)
Die Size
2935 × 2935 µm
Core Area
2051 × 2051 µm
Channels
32 frequency channels
Data Width
16-bit per channel
Threshold Range
16 – 1024 (adaptive)
Timestamp
32-bit
FIFO Depth
16 entries
Output Protocol
AER (Address Event Representation)
Padring
60 × Analog + 20 × Bidir + 4×DVDD + 4×DVSS
Clock
25 MHz (CLOCK_PERIOD = 40ns)
Tools
LibreLane 3.0 + OpenROAD + Yosys + Magic/KLayout

## Slide 5
Build Results — LibreLane 3.0 Signoff
0
Lint Errors
0
Timing Violations
~130K
Instances
7.8M µm²
Design Area
0.018 W
Total Power
40 ns
Clock Period
⚠ Known issues: 2470 max_slew violations at SS corner (125°C, 4.5V) — fix in progress

## Slide 6
Chipathon 2026 — Key Milestones
Jun 26
Analog Design Ideas
Jul 3
Schematic Review
Jul 10
Simulation Review (blocks)
Jul 17
Simulation Review (top) + Go/No-go
Jul 24–Aug 7
Layout Tutorials + DRC Dry-run
Aug 14–21
Layout Reviews
Aug 28
Verification + Final Chip Review
TBD
Final GDS Submission

## Slide 7
Thank You
TeamVKU — SSCS Chipathon 2026 — Track A SFE Audio Frontend: 32-Channel Spiking Frequency Encoder
github.com/hoangvu10105/chipathon-2026-teamvku
Discord: SSCS Chipathon → #2026-track-a-foundational-building